## Slide 1: Virtual Memory
prepared and instructed by
Shmuel Wimer
Eng. Faculty, Bar-Ilan University

## Slide 2: Motivation
Virtual memory (VM): A technique using main memory as a “cache” for secondary storage (disk).
Consider a collection of programs is simultaneously running on a computer.
The total required memory is much larger than the amount of main memory.
Main memory needs to contain only the active portions of the programs.
The principle of locality applies.

## Slide 3
Virtual memory:
Allows efficient and safe sharing of memory among multiple programs.
Removes the programming burdens of a small, limited amount of main memory (past, less relevant today).
VM allows to efficiently share the processor and the main memory.
We must be able to protect the programs from each other.
A program can only read and write the portions of main memory that have been assigned to it.

## Slide 4
The programs sharing the memory change dynamically while the programs are running. The compiler sets each program into its own address space.
VM translates the program’s address space to physical addresses, enforcing protection of a program’s address space from other programs.
VM allows a single user program to exceed the size of primary memory.
A VM block is called a page, and a virtual memory miss is called a page fault.
VM produces a virtual address, translated by a SW and HW combination to a physical address.

## Slide 5
virtual pages
physical pages

## Slide 6: Virtual to Physical Address Mapping
4KB page size
220 virtual pages
4GB
4KB page size (frame)
218 physical pages (frames)
1GB
Illusion of an unbounded amount of virtual memory.

## Slide 7
Design choices in VM systems are motivated by the high cost of page fault, taking millions of clock cycles to process.
Pages should be large enough to amortize the high access time. Size ranges from 1 KB (embedded), 16 KB (PC) to 64 KB (severs).
Organizations that reduce the page fault rate, e.g., fully associative placement of pages in memory.
Page faults can be handled in SW because the overhead will be small compared to the disk access time. SW can use smart algorithms for page placement.
Write-through will not work for VM, since writes take too long. VM uses write-back.

## Slide 8: Placing a Page and Finding it Again
Reducing page fault frequency is critical due to the high page fault penalty.
The operating system (OS) maps the virtual to any physical page (associative placement of pages).
The OS can use smart algorithms and complex data structures to track page usage.
A page table stored in memory, indexed by the virtual page number, contains the virtual to physical address translations.
An entry contains the physical page number for that virtual page if the page is currently in memory.

## Slide 9
To indicate the location of the page table in memory, the hardware includes a page table register, pointing to the start of the page table.
The page table + PC + registers specify the state of a program (process). To allow another program to use the processor, this state is saved. Restoration of this state enables the program to continue execution.
A process is active when it is in possession of the processor. Otherwise it is inactive.
OS activates a process by loading the process's state, including the PC.

## Slide 10
The process’s address space, and hence all the data it can access in memory, is defined by its page table, residing in the memory.
The OS needs to load only the page table register with the pointer to the table of the process to be run.
Each process has its own page table (+register), since different processes use the same virtual addresses.
The OS allocates the physical memory and updates the page tables, to avoid collision of the virtual address spaces of different processes.
Separate page tables provide protection of one process from another.

## Slide 11
OS algorithm determines the physical page number.
The page table
Each process has such register.

## Slide 12
The OS creates the space on disk for all the pages of a process when it creates the process.
This disk space is called the swap space.
OS also creates a data structure to record where each virtual page is stored on disk.
It may be part of the page table or an auxiliary data structure indexed in the same way as the page table.
The physical page bit-width is extended to 32 for ease of indexing. The extra bits are used to store additional information.

## Slide 13
The page table maps each VM page to either a page in main memory or a page stored on disk.
Virtual page number is used to index the page table.
Valid bit 0: the page currently resides only on disk, at a specified disk address.

## Slide 14
OS handles data structure to track which processes and which virtual addresses use each physical page.
The OS is another process, and these tables controlling memory reside in memory.
When all the pages in main memory are in use, the OS chooses a page to replace. Replaced pages are written to swap space on the disk.
To minimize the number of page faults LRU is used. But it is too expensive, requiring updating a data structure on every memory reference. Instead, an approximation is used.

## Slide 15
Some computers provide a use bit or reference bit, (in HW) which is set whenever a page is accessed.
OS periodically clears the use bits and records them. It can determine which pages were touched during a certain time period.
OS then evicts a page whose reference bit is off.
With 32-bit virtual address, 4 KB page size, and 4 bytes per page table entry, the total page table size is: # page table entries = 232 / 212 = 220.
Size of page table = 220 x 4bytes = 4MB (for every process! There may be 100’s!)

## Slide 16: Writes in Virtual Memory
Access time difference between cache and main memory is 10’s – 100’s cycles. Write-through with a write buffer to hide the latency of the write from the processor worked.
In a VM system, writes to disk take millions processor cycles, so write-through is impractical.
Write-back, called copy back, is copying the page back to disk when it is replaced in the memory.
Disk transfer time is small compared to access time, so copy back is far more efficient than write-through.

## Slide 17
A write-back is still costly.
We would like to know whether at a replacement the page needs to be copied back.
A dirty bit is added to the page table, being set when any word in a page is written.
The dirty bit indicates whether the page needs to be written out before its location in memory can be given to another page.

## Slide 18: Fast Address Translation: The TLB
The page tables are stored in main memory. Every memory access by a program is thus twice long:
One access to obtain the physical address (from page table),
a second access to get the data (elsewhere in memory).
Locality of reference to the page table can help:
A translation for a virtual page number will probably be needed again soon, because references to the words on that page have both temporal and spatial locality.
A special cache, called Translation Look-aside Buffer (TLB), keeps track of recently used translations.

## Slide 19
We access the TLB on every reference instead of the page table. TLB must therefore include the valid, dirty and the reference bits.
TLB

## Slide 20
A TLB miss can be either a true page fault or just a TLB miss. If the page exists in memory, the processor loads the translation from the page table into the TLB and tries the reference again.
Every reference looks up the virtual page # in TLB.
TLB hit uses the physical page # to form the address and turns on the reference bit. Write turns on the dirty bit too.
In a true page fault the processor invokes the OS (exception).
TLB has much fewer entries than pages in main memory. TLB misses are therefore much more frequent than page faults.

## Slide 21
At TLB miss we need to select a TLB entry to replace and copy the reference and dirty bits back to the page table entry. Those are the only TLB entry portion that can be changed.
Typical values for a TLB
TLB size: 16–512 entries
Block size: 1–2 page table entries (typically 4–8 bytes each)
Hit time: 0.5–1 clock cycle
Miss penalty: 10–100 clock cycles
Miss rate: 0.01%–1%
Write-back copies entries back from TLB at miss time rather than when they are written (dirty, reference). It is very efficient since TLB miss rate is small.

## Slide 22
Real TLB Read
TLB
cache
Physical address
Virtual address

## Slide 23
4 KB page
20 bit virtual page #
32 bit address Space
TLB entry is 64 bits:
20-bit tag (virtual page # for that TLB entry), corresponding physical page # (also 20 bits), valid bit, dirty bit, and other bookkeeping bits.
physical address generation
Fully associative 16-entries TLB, shared between instruction and data references.

## Slide 24
16KB cache
Detected cache hit
read from cache

## Slide 25: Read and Cache Write-Through
Cache
write-through
Best case

## Slide 26
What happens at MIPS TLB miss? First, the page # of the reference is saved in a special register (for the OS).
The OS handles the miss in SW (exception). The routine indexes the page table using the page # of the virtual address and the page table register (stores the starting address of the active process page table).
Using a special set of system instructions that can update the TLB, the OS places the physical address from the page table into the TLB.
TLB miss takes 13 clock cycles, assuming the OS code and the page table entry are in the instruction and data caches.
A true page fault occurs if the page table entry does not have a valid physical address.

## Slide 27: VM, TLBs and Caches Integration
VM and cache work together as a hierarchy. Data must be in main memory if it is in the cache.
OS maintains this hierarchy by flushing the contents of any page from the cache upon deciding to migrate that page to disk.
The OS modifies the page tables and TLB accordingly. An attempt to access any data on the page generates a page fault.
In best case, a virtual address is translated by the TLB and sent to the cache where the appropriate data is found, retrieved, and sent back to the processor.

## Slide 28
In the worst case, a reference can miss all: the TLB, the page table, and the cache.
Consider all the seven combinations of the three events. State for each whether it can actually occur and under what circumstances.

## Slide 29: Virtually Addressed Cache
All memory addresses were translated to physical addresses before the cache was accessed. The cache is thus physically indexed and physically tagged.
Assuming a cache hit, the time to access memory must accommodate both a TLB and a cache accesses. These two accesses can of course be pipelined.
The processor can alternatively index the cache with an address that is completely or partially virtual.
It uses tags that are virtual addresses. Such a cache is virtually indexed and virtually tagged.

## Slide 30
The address translation hardware (TLB) is therefore unused during the normal cache access, taking the TLB out of the critical path, thus reducing cache latency.
In a cache miss however, the processor needs to translate the address to a physical address so that it can fetch the cache block from main memory.
When the cache is accessed with a virtual address and pages are shared between programs, aliasing may occur by two virtual addresses for the same page.
A word on such a page may be cached by two different virtual addresses, allowing one program to write the data without the other program being aware of it.

## Slide 31
A compromise is caches that are virtually indexed but physically tagged.
It attempts to achieve the performance of virtually indexed caches with the architecturally simpler physically addressed cache.